## Slide 1: MEGC MATLAB Technical Workshop
Denislav Nikolov
October 29th , 2020

## Slide 2: Workshop Outline
Part 1: MATLAB Basics/Recap (~50 min)
  Why MATLAB?
  Programming Basics
  MATLAB Interface
  Plotting
  Helpful functions and tools
  Additional Resources
Break (~10 Min)
Part 2: MATLAB Problem Solving (~1 Hour)
  3 Application Problems
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 3: Part 1: Fundamentals
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 4: Why MATLAB?
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 5: What is Engineering?
MEGC MATLAB Technical Workshop
October 29th, 2020
Input (tools, equations)
Function (engineer, program)
Output (structure, vehicle)

## Slide 6: MATLAB is Like Us
MEGC MATLAB Technical Workshop
October 29th, 2020
Input
Function
Output
MATLAB has a nearly infinite library of functions
[output] = function(input)
MATLAB can deal with large quantities of data in convenient matter
. . .
A =
[graph] = dodec(A)

## Slide 7: MATLAB Interface
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 8: Navigating the UI
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 9: Navigating the UI
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 10
MEGC MATLAB Technical Workshop
October 29th, 2020
Basic Commands
To clear your command window: clc
To close all figures: close all
To clear your workspace: clear all
To stop a runaway code: ctrl+c
To comment out a line of code: % (at beginning)
To comment out a block of code:
Highlight, then ctrl+r
To comment in a block of code:
Highlight, then ctrl+t

## Slide 11: … and the most useful command
MEGC MATLAB Technical Workshop
October 29th, 2020
If you don’t know how to use a built-in command or function:
>> help myFunction
And remember, Google is your best friend!

## Slide 12: MATLAB Basics
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 13: Variable Types
MEGC MATLAB Technical Workshop
October 29th, 2020
Most of the time, you won’t need to explicitly define these
Characters:
Complex numbers:
Decimal numbers:
Integer numbers:
Logic statements (T/F):
Structures:
char,string
complex
double/single
int8,int16,uint8
logical
struct

## Slide 14: Variable Types: MATLAB Auto Recognition
MEGC MATLAB Technical Workshop
October 29th, 2020
‘data’,”data”
num + num*i
num.12345
Explicit
Explicit
Explicit
char,string
complex
double/single
int8,int16,uint8
logical
struct

## Slide 15: Variable Types: Converting
MEGC MATLAB Technical Workshop
October 29th, 2020
Converting from numerical data types
Rounding regularly, up, or down values
Other functions:
double(input), num2str(inpt)
round(input,n)
floor(input)
ceil(input)
string(input)
int2str(input)
str2double(input)

## Slide 16: Logic Statements
MEGC MATLAB Technical Workshop
October 29th, 2020
Logic statements are crucial towards decision making processes in programs
Run code if condition is true
Run code if other condition is true
Run code for any other non-stated condition
if statement
run code...
elseif statement
run code...
else
run code...
end

## Slide 17: Logic Statements: Operators
MEGC MATLAB Technical Workshop
October 29th, 2020
These operators output a value of true or false based on properties of a variable in question.
Relational (comparison) operators:
  Less/greater than: >, >=, <, <=
  Equal/not equal: ==, ~=
  (use = for assignments only)
Logical operators
  Used in decision-making, array indexing, etc.
  AND: && (& for whole arrays)
  OR: || (| for whole arrays)

## Slide 18: Logic Statements: If-Else Example
MEGC MATLAB Technical Workshop
October 29th, 2020
if i == 1
disp 'Hello World';
elseif i > 2
disp 'Hello Other World';
else
disp 'Hello You';
end

## Slide 19: Logic Statements: While Loops
MEGC MATLAB Technical Workshop
October 29th, 2020
Warning: While loops have a danger of being endless. Press Ctrl+C to end code in MATLAB
Run code while condition is true
while statement
run code...
end
i = 0;
while i > 1
disp 'Hello World'
i = i + 0.5;
end

## Slide 20: Logic Statements: For Loops
MEGC MATLAB Technical Workshop
October 29th, 2020
For loops will most likely help with the potential infinite loop problem presented in the while loop
Run code continuously between a range of values
for range
run code...
end
for i = 1:10
disp 'Hello World'
end

## Slide 21: Matrices/Vectors
MEGC MATLAB Technical Workshop
October 29th, 2020
Matrices are multidimensional groups of indexed doubles. Matrices are the core of MATLAB computing.
Build arrays using brackets ([]) with commas or spaces between entries within the same row and semicolons (;) to start a new row.
Vectors are m × 1 or 1 × n -dimensional arrays. Vectors are often defined by themselves or they can be created by taking a part of a column or row of a larger array using the colon (:) operator.

## Slide 22: Matrices/Vectors: Indexing and Slicing
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 23: Matrices/Vectors: Indexing and Slicing
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 24: Matrices/Vectors: Indexing and Slicing
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 25: Matrices/Vectors: Indexing and Slicing
MEGC MATLAB Technical Workshop
October 29th, 2020
6
8
4
7

## Slide 26: Matrices/Vectors: Combining Two Vectors
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 27: Matrices/Vectors: Combining Two String Vectors
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 28: Variables Types – Cell Arrays
MEGC MATLAB Technical Workshop
October 29th, 2020
Cell Arrays are multidimensional groups of indexed data containers. Cell arrays are a powerful extension of the normal array, as each cell may contain any data type and can be any size.
Build cell arrays just like you would normal arrays, except use braces ({}) instead of brackets ([]).
>> a = linspace(1, 10, 10);
>> b = ’my string’;
>> c = 2;
>> d = [1, 2; 3, 4];
>> B = {a, b; c, d};
B =
2×2 cell array
{1×10 double} {'my string'}
{[ 2]} {2×2 double }

## Slide 29: Matrices/Vectors: Lin. Algebra
MEGC MATLAB Technical Workshop
October 29th, 2020
For computations involving vectors and arrays, often you must use the elementwise operator (.)
>> A = [1, 4, 9; 16, 25, 36; 49, 64, 81];
>> A^2
ans =
506 680 882
2180 2993 3960
5042 6980 9306
>> A.^2
ans =
1 16 81
256 625 1296
2401 4096 6561

## Slide 30: Functions: Useful Functions
MEGC MATLAB Technical Workshop
October 29th, 2020
MATLAB has a nearly infinite library of functions
[output] = function(input)
Plot:
Numerical integration:
Backward Slash (Ax=b):
Array of Zeros (m X n):
Identity Matrix (m X m):
Vector of Linearly Spaced-Points (ab):
plot(x,y)
integral(fun,a,b)
X = A\b
zeros(m,n)
eye(m)
linspace(a,b,n)

## Slide 31: Functions: User-defined Functions
MEGC MATLAB Technical Workshop
October 29th, 2020
The name of the function must match the name of the m-file in which it lives – MATLAB will warn you if it is not
[output] = function(input)
function [output1,output2,…] = func_name(arg1,arg2,…)
statements
end

## Slide 32: Plots: 2-D Plots
MEGC MATLAB Technical Workshop
October 29th, 2020
  MATLAB is very often used to generate plots. To generate a 2-D line plot, use the following syntax:
  plot(x,y,‘name’,value,…)
  where the ‘name’,value pairs are used to configure the individual features of the line. Other plot features are controlled using related functions that are called independently. For example:
  plot(t, sin(t), ‘r-’)
  plot(x,y,’Linewidth’,2)
  xlabel(‘time’)
  legend(‘Trial 1’, ‘Trial 2’)

## Slide 33: Plots: Other Plots to Explore
MEGC MATLAB Technical Workshop
October 29th, 2020
Scatter plot:
Histogram:
3D plot:
3D scatter plot:
Plots (n X m) in 1 figure:
Log plot:
Semilog plot:
Polar coordinate plot:
scatter(x,y)
histogram(x)
plot3(x,y,z)
scatter3(x,y,z)
subplot(n,m,i)
loglog(x,y)
semilogx(x,y)
semilogy(x,y)
polarplot(θ,r)

## Slide 34: Plots: Other Function Plots
MEGC MATLAB Technical Workshop
October 29th, 2020
Label x/y axis:
Title your plot:
Title your figure:
Change axis sizes:
xlabel(‘name’)
ylabel(‘name’)
title(‘name’)
sgtitle(‘name’)
axis([xmin xmax ymin ymax])
xlim([xmin xmax])
ylim([ymin ymax])

## Slide 35: Plots: 2-D Plots Example
MEGC MATLAB Technical Workshop
October 29th, 2020
t = 0:0.01:2*pi();
y1 = sin(t);
y2 = cos(t);
plot(t,y1)
hold on
plot(t,y2, 'r-','Linewidth',2)
xlabel('Time')
ylabel('Amplitude')
legend('Sin(t)','Cos(t)')
title('MATLAB Plotting Example $$\lambda_{Awesome}$$','Interpreter','latex')

## Slide 36: Plots: 3-D Plots Example
MEGC MATLAB Technical Workshop
October 29th, 2020
scatter3(x,y,z)

## Slide 37: Helpful Functions and Tools
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 38: Symbolics Functions
MEGC MATLAB Technical Workshop
October 29th, 2020
Declare your function
and variables
Integral
Derivative
Step function
Plot syms function
Solve for a variable
Plug value into variable
syms f
syms x y
int(f,x,[a b])
diff(f,x)
heaviside(x)
fplot(f)
solve(f,x)
subs(f,x,a)
Syms functions allow you to manipulate equations

## Slide 39: Symbolics Functions: Example
MEGC MATLAB Technical Workshop
October 29th, 2020
syms x y z
f(x,y,z) = x^2 + y^2 + z^2;
Derivative
>> diff_T = diff(f,x)
diff_T(x, y, z) =
2*x
Definite Integral
>> int_T = int(f,x,[0 1])
int_T(y, z) =
y^2 + z^2 + 1/3
Solving for x
>> what_is_x = solve(f,x)
what_is_x =
(- y^2 - z^2)^(1/2)
-(- y^2 - z^2)^(1/2)

## Slide 40: Publish (Nice PDF)
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 41: Publish (Nice PDF)
MEGC MATLAB Technical Workshop
October 29th, 2020
Page 1
Page 2

## Slide 42: Simulink
MEGC MATLAB Technical Workshop
October 29th, 2020
Method of solving Ordinary Differential Equations with block diagrams to solve for ODE

## Slide 43: Simulink
MEGC MATLAB Technical Workshop
October 29th, 2020
Method of solving Ordinary Differential Equations with block diagrams to solve for ODE

## Slide 44: Excel Editing and Reading
MEGC MATLAB Technical Workshop
October 29th, 2020
xlsread('Filename.xls’)
writetable(A ,'Filename.xls’)

## Slide 45: Additional Resources
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 46: Additional Resources
MEGC MATLAB Technical Workshop
October 29th, 2020
Practical Guide to MATLAB & Simulink for Engineers
  1-hour refresher course with asynchronous examples
Control Tutorials for MATLAB & Simulink (U-Mich)
  Modules include lectures and examples to systems (modeling, analysis), controls (PID, root locus, frequency, digital controls, state-space) and Simulink (modeling, control, simscape)
Official MathWorks MATLAB and Simulink Training
  Formal courses in MATLAB, Simulink and Image Processing.
  Potential certifications

## Slide 47: 10 Minute Break/Q&A
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 48: Part 2: Application
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 49
MEGC MATLAB Technical Workshop
October 29th, 2020
Programming Flowchart
Step 1:
Input/Output?
Step 2:
If/for/while?
Step 3:
Functions?
Step 4:
Drawing
Step 5:
Start Coding
Step 6:
Debug

## Slide 50
MEGC MATLAB Technical Workshop
October 29th, 2020
Programming Flowchart
Step 1:
Input/Output?
Step 2:
If/for/while?
Step 3:
Functions?
Step 4:
Drawing
Step 5:
Start Coding
Step 6:
Debug

## Slide 51
MEGC MATLAB Technical Workshop
October 29th, 2020
Programming Flowchart
Step 1:
Input/Output?
Step 2:
If/for/while?
Step 3:
Functions?
Step 4:
Drawing
Step 5:
Start Coding
Step 6:
Debug
Are there
need for
iterations?
Do I need
to meet any
conditions?
Are iterations
finite or
conditional?

## Slide 52
MEGC MATLAB Technical Workshop
October 29th, 2020
Programming Flowchart
Step 1:
Input/Output?
Step 2:
If/for/while?
Step 3:
Functions?
Step 4:
Drawing
Step 5:
Start Coding
Step 6:
Debug

## Slide 53
MEGC MATLAB Technical Workshop
October 29th, 2020
Programming Flowchart
Step 1:
Input/Output?
Step 2:
If/for/while?
Step 3:
Functions?
Step 4:
Drawing
Step 5:
Start Coding
Step 6:
Debug

## Slide 54
MEGC MATLAB Technical Workshop
October 29th, 2020
Programming Flowchart
Step 1:
Input/Output?
Step 2:
If/for/while?
Step 3:
Functions?
Step 4:
Drawing
Step 5:
Start Coding
Step 6:
Debug

## Slide 55
MEGC MATLAB Technical Workshop
October 29th, 2020
Programming Flowchart
Step 1:
Input/Output?
Step 2:
If/for/while?
Step 3:
Functions?
Step 4:
Drawing
Step 5:
Start Coding
Step 6:
Debug

## Slide 56: Examples (Open up LiveScript File)
MEGC MATLAB Technical Workshop
October 29th, 2020

## Slide 57: For Questions or Comments, Contact:
dnikolov@umich.edu
Get to coding!
MEGC MATLAB Technical Workshop
October 29th, 2020